| LD-440 |  | Page I of3 |
| --- | --- | --- |
| (5-17-10) |  |  |
|  | DEPARTMENT OF TRANSPORTATION |  |
|  | LOCATION AND DESIGN |  |
|  | DESIGN EXCEPTION REQUEST |  |
|  | (Note: Use the Tab key to navigate and complete the Form) |  |

To: Bart Thrasher, P.E. Date: 1-21-2011Assistant State Location and Design Engineer Mr. John. Lynch, P.E. From: Regional Transportation Program Director Drop-down Selection Subject: DESIGN EXCEPTION REQUEST DE-l FOR REDUCED SHOULDER WIDTH

Prepared by: Zhen Feng, P.E, PhD

(FO)0095-96A104, C501, B658 State Project Number: thru B667 Federal Project Number: NH-095-2(489)

Prince William State County/City: &Fairfax. District: NO. VA. Funding Source: /FHWA

-~--...;....-

Project Description From: 0.015Mile South of Route 123 UPC: 57017 To: 0.154 Mile North ofRoute 7100

Design Exception Request For:D Design Speed 0 Horizontal Clearance· o Vertical Clearance· (other than "clear zone")

~ Bridge Width· o Horizontal Alignment o Vertical Alignment

o 	LaneWidth o Sight Distance o Cross Slope

~ 	Shoulder Width o Superelevation o Grade Structural o Interstate Access Control o Other

o 	Capacity·

• These are typically requested by the Bridge designer.

Current ADT: 205,000 (2006) Design ADT: 239,000 (2030)

% Trucks: 11% Design Speed: 60 MPH Posted Speed: 60 MPH

Reduced Design Speed (ifapplicable) _N_/_A Is Project on the NHS? Yes Urban Interstate Functional Classification: _(:..,.1-_9_5,,-) Min. VDOT GS Standard: Rt ShIdr = 12ft

Min. AASHTO Standard: 12 ft

-=:....=.:..._----

Existing Dimensions Rt Shldr 12ft Min Requested Dimensions Rt Shldr 3 ft Min

Total estimated construction cost ofproject: $ 500,000

(Based on approval ofthis exception)

(

In excess of$ 3,800,000 to meet min standards on both lane and shoulder

Additional cost to meet minimum AASHTO standard: _w.....;;.;;id;..;.;th;;.;..•(E;;.;.xh;;;;;;;;..;ib;.;;.it;..;D;;..)'--	_

LD-440 Page 2 of 3 (5-17-10) Background description ofproject: (Attach Separate Document) (Include a description ofthe general characteristics ofthe existinghighway focusing on the featuresrelevanttotheproposedexception. Providea briefdescriptionoftheadjacenthighway segments, highlighting existing nonstandard features when relevant to the proposed exception as well as the title sheet, typical section sheet, applicable plan sheets, profiles and cross sections.)

Purpose and need for exception; why standards cannot be met (include any future plan to upgrade this exception to standard):

See attachment.

Are there any plans to improve the approach roadway within the next ten (10) years? _N_o _

Accident history for the past 3 years:

See attachment.

Effect ofdesign exception on safety:

See attachment.

Any mitigation ofthe substandard design element (s):

See attachment.

Has the Regional Traffic Engineer reviewed the substandard design and do they agree with the proposed mitigation measures? Ifnot, please explain. Yes.

LD-440 Page 3 of3 (5-17-10)

VDOT GEe for VA Megaprojects Alexandria, Virginia Civil En ineerin

| Submitted By: | Zhen Feng, PE, PhD | Date: | 1-21-2011 |
| --- | --- | --- | --- |
|  | Consultant |  |  |
| Remarks: |  |  |  |

Recommended for Approval By: Bart Thrasher, P.E. Date: Assistant State Location and Design Engineer and Recommended for Approval By: Date: State Traffic Engineer (For Crossovers Only)

| Remarks: |
| --- |
| VDOT Approval By: | Mr. Mohammad Mirshahi, P.E. | Date: | ------ |
| State Location and Design Engineer |  |  |
| FHWA Approval By: | Date: |  |
| Remarks: |  |  |
| Cc: | Project Manager |  |  |
| Project Designer |  |  |
| QMAC Section Manager |  |  |

Attachment to DE-l Reduced Shoulder Width

Background Description of Project:

The existing acceleration lane for the southbound ramp from EB Route 123 to SB 1-95 is only 350 feet long, which does not meet AASHTO and VDOT road design standards.

The proposed SB 1-95 Route 123 ramp improvements will be constructed in conjunction with the 1-95 Fourth Lane Widening project and will extend the existing acceleration lane to AASHTO and VDOT standards. Proposed pavement work will be limited within the existing 1-95 SB pavements. Part of the existing shoulder is to be reconstructed with full-depth pavement and restriped to provide a ramp acceleration lane. As a result, the existing ramp acceleration lane length will be increased from 350 feet to 1,200 feet (According to the AASHTO Green Book [2004], a 1,200-foot acceleration lane, plus 300-foot taper is preferred because this ramp is often carrying traffic volumes equal to the capacity ofthe merge).

Purpose and Need for Exception; Why Standards Cannot be Met (include any future plan to

upgrade this exception to standard):

The purpose ofthis design exception is to provide increased acceleration distance to meet current AASHTO standards by extending the acceleration lane within the available cross-section width without pavement and bridge widening, which results in a substandard lane and shoulder width for the length of the extension.

The minimum existing pavement width (face-to-face of barriers, including the bridge over Occoquan Road) is about 57 feet, with the following lane configuration:

8ft Lt. Shoulder + 3 @ 12ft GP Lanes + Min 13ft Rt. Shoulder

To accommodate the extension of the acceleration lane within the existing footprint, the existing right shoulder in this area will be reconstructed with full-depth pavement, and approach slabs will be added at the bridge. In addition, part of existing 1-95 SB most right side GP lane will be resurfaced and restriped. The new lane configuration will be as follows:

8ft Lt Shoulder + (12ft + 12ft +11ft) GP Lanes + 11ft Acceleration Lane + Min 3ft Rt. Shoulder

The standard shoulder and lane widths cannot be provided without widening the existing bridge, relocating the existing sound wall, and constructing new fill areas or a retaining wall within the border area between the sound wall and right-of-way. In addition, the preliminary engineering study indicates that a minimum 3-foot right shoulder is required to provide adequate drainage spread across the shoulder. If all the lane widths were to be maintained as 12 feet, there would be only 1 foot available for the shoulder. Therefore, to accommodate the new auxiliary lane within the existing dimensions, the total travelway width will have to be reduced 2 feet within the length of the improvements.

The outside two lanes were chosen for reduction because the new auxiliary lane would provide full-pavement depth refuge for any drift from the proposed II-foot GP lane. The existing inside shoulder is not full-depth pavement, so reducing the inside lane to 11 feet was not considered.

lof5

Attachment to DE-l Reduced Shoulder Width

In summary, the standard lane width cannot be maintained without widening the existing bridge, relocating the existing sound wall, and constructing new fill areas a or retaining wall within the border area between the sound wall and right-of-way. There is very limited available space between the existing 1-95 median barrier and sound wall. Relocation of the existing sound wall and widening the existing 1-95 SB lanes and bridge (B648, over Occoquan Road) to provide additional pavement width to accommodate the acceleration lane extension would result in additional right-of-way takes for construction easements and large amount of retaining wall installation. Other design concerns include:

Additional impervious areas and relocation of the sound wall require an environmental impact assessment.

Additional storm surface runoff generated from additional impervious areas requires evaluation and/or improvement of existing stormwater management practices, including adequate outfall analysis and potential floodplain study.

Bridge widening will have major impact on the existing Occoquan Road, especially because the existing minimum vertical clearance at the 1-95 SB Bridge over Occoquan Road is 15'9". Widening the existing 1-95 SB bridge will further reduce the vertical clearance.

Existing ramp lighting is located between the barrier and sound wall.

To minimize the right-of-way and environmental impacts, and overall project footprint, nominal reductions in the two inside right lanes are proposed and a reduction in the right shoulder width is proposed (approximate) from Sta 131+75 to 146+75.

A separate design exception DE-2 is submitted for the reduced lane widths. All other roadway geometric design elements meet design standards.

In addition, based on discussion with the State Structure and Bridge Engineer (see Exhibit F), the TL-4 New Jersey Shape bridge parapet, which was installed during 1997 bridge widening project and passed the annual safety inspection this year (see Exhibit G), would remain in place. In accordance with VDOT's Structure and Bridge Manual, Vol. V, Part 2, File No 25.02-4 (August 2009, see Exhibit K), any bridge on the interstate with an ADT of more than 39,000 vehicles, 11% to 15% truck volume, and 60 mph design speed would require a parapet tested to TL-5, even with a 12-foot shoulder. However, based on the accident history analysis (provided in the following section), and considering that at the end of the project, the improvements will result, overall, in a safer facility (i.e, the benefits of extending the acceleration lane would far exceed any risks associated with a reduced shoulder or a parapet that is not tested to the crash level TL-5 requested), and considering the additional cost of widening the bridge and replacing the existing parapet and sound barrier wall, we recommend maintaining the existing parapet and barrier along the ramp acceleration lane during this improvement.

2of5

Are there any plans to improve the approach roadway within the next ten (10) years? -No.

(

Widening 1-95 to four lanes in each direction is in the Prince William County Transportation Plan but is not in the MWCOG CLRP.

The 1-95 SB bridge over Occoquan Road was installed at 1962 and widened in 1997. As noted in the most recent inspection report, the bridge is in fair condition, with a sufficiency rating of 81, a deck rating of 6, superstructure rating of 5, and a substructure rating of 6. The inspection report also provides the following recommendations for intermediate and long-term repairs for the bridge:

Intermediate term recommendations:

Cover and protect exposed electrical wires and replace rusted junction box at Pier 2,1 EA.

Repair edge spalls, clean, and reseal expansion joints, 722 LF.

Seal cracks in the top ofthe deck, 1,400 LF.

Reset Bearings 1 through 7 in Span 2 at Pier 1 and Span 3 at Pier 2, 14 EA.

Shim bearing under Girder 3 in Span 2 at Pier 2, 1 EA.

Clean and spot paint girders, 630 LF.

Clean and spot paint bearings and diaphragms, LS.

Replace parapet reflectors, 12 EA.

Long-term repair recommendations:

Repair spalled and/or delaminated areas in the bottom ofthe deck, 148 SF.

Repair spalled and/or delaminated areas in the abutments, 9 SF.

Repair spalled and/or delaminated areas in the pier caps, 77 SF.

Repair spalled and/or delaminated areas in the pier columns, 25 SF.

Remove tree branches overhanging the southbound roadway shoulder, LS.

Noneoftheserecommendedrepairswouldfall intothecategory ofmajorrehab. Amajorrehab project for this bridge (such as deck replacement) will not be required within the next 20 to 30 years. However, before any major rehab work is scheduled on this bridge, VDOT will consider widening the bridge at that time.

Accident History for the Past 3 Years:

Accidents occurring between 2004 and 2008, for the portion ofI-95 between the SB 123 ramp

gore to the end ofthe proposed acceleration lane only, are shown in the attached table, Accident

History. Atotal of29crashesinthisareahavebeenreportedbetween2006 and2008. Ofthese,

no fatalities have been reported, and 10 injury accidents were reported. Sixty-six percent of all

accidents are rear-end accidents (19) followed by side swipe (8, or 28 percent ofall accidents).

More than 93 percent ofcrashes can be associated with backups and short merge lengths linked

to inadequate acceleration lane length. See the following Summary Table and Exhibit C.

30f5

Attachment to DE-l Reduced Shoulder Width

| Crash Type |
| --- |
| YEAR | Fixed Object | Rear End | Side Swipe | Deer | Overturn | CRASH ACCOUNT | INJUR ACCOUNT |
| 2004 | 0 | 2 | 2 | 0 | 0 | 4 | 4 |
| 2005 | 2 | 2 | 1 | 1 | 0 | 6 | 3 |
| 2006 | 0 | II | 2 | 1 | 0 | 14 | 4 |
| 2007 | I | 4 | 5 | 0 | 0 | 10 | 5 |
| 2008 | 0 | 4 | 1 | 0 | 0 | 5 | 1 |
| 2006 to 2008 Subtotal | 1 | 19 | 8 | 1 | 0 | 29 | 10 |
| Total | 3 | 23 | 11 | 2 | 0 | 39 | 17 |

Effect of Design Exception on Safety:

The existing bridge parapet is on the right shoulder ofthe acceleration lane. The horizontal clearance between the right inside GP lane and barrier actually has been increased (from 13 feet to 14 feet minimum) within the length of the improvements.

Any Mitigation of the Substandard Design Element(s):

The suggested mitigation strategies in FWHA's Mitigation Strategies For Design Exceptions (July 2007) for urban facilities are signing, delineation, enhanced pavement markings, and lighting. Additional signing does not seem feasible for this short segment because ofthe inability to sign only two ofthe four lanes. However, enhanced pavement markings (6-inch pavement striping) and delineation are feasible and will be provided and the ramp has existing lighting.

Additional mitigations also include:

Place delineators on the existing barrier to enhance a driver's ability to stay within the lane.

Hatch the proposed substandard shoulder area that will be only 3 feet wide (approximately 100 feet ofthe acceleration ramp).

Miscellaneous Issues

Existing Barrier and Bridge Parapet

The existing parapet barrier on the 1-95 SB bridge over Occoquan Road, installed during the 1997 bridge widening project, has just passed the VDOT annual safety inspection (See Exhibit G, Bridge Inspection Report, 2010). Base on our field observation and measurement, it is and Fshape NCHRP Report 350-approved TL-4 (FHWA's Roadside Hardware Policy and Guidance; see Exhibits J, K and L). The adjacent roadway barrier is consistent with the bridge parapet and also meets NCHRP 350 standards.

40f5

Attachment to DE-1 Reduced Shoulder Width

However, based on VDOT's Structure and Bridge Manual, Vol. V, Part 2, File No 25.02-4 (August 2009), which was developed based on a FHWA April 1994 unpublished fmal report, any bridge on the interstate with a design ADT of239,000 vehicles (for year 2030), 11% truck volume, and 60 mph design speed would require a parapet tested to TL-5, even with a 12-foot shoulder.

A number ofmeetings and discussions have been held between design engineers and VDOT Regional Transportation Program Director, 1-95 Fourth Lane Widening Project Manager, and structure and bridge engineers. Engineering review and evaluation of existing bridge parapet and barriers within the project limits have also been conducted. It has been decided that the existing barrier and bridge parapet within the construction limits will remain in place, based on the following reasons:

1) 	Most ofthe accidents over last 5 years are rear-end accidents. Even though the reduced lane width may have an impact on the side-swipe accident statistics, overall, improvements to the acceleration and merging length ofthis ramp should reduce the total number of accidents.

2) 	At the end ofthe project, the improvements will result in an overall safer facility (i.e., the benefits ofextending the acceleration lane would far exceed any risks associated with a reduced shoulder or a parapet that is not tested to the crash level TL-5 requested).

3) 	The additional cost associated with widening bridge and replacing the existing parapet and sound barrier wall should also be taken into account during the engineering decision on the existing barriers.

4) Existing bridge parapets within the construction limits comply with the guidelines and specifications for the bridge widening in the 1-95 Fourth Lane Widening Project.

5) 	The adjacent barrier type is consistent with existing bridge parapet type.

Impact on the Emergency Vehicle Access

Existing Condition: Currently along this ramp (from Route 123 eastbound to 1-95 southbound), a driver can use the existing 13-foot shoulder. Please note that immediately north and south ofthis ramp, the mainline shoulders are 12 feet or more. However, on the upstream Route 123 WB to 195 SB loop ramp (about 19 feet wide) the acceleration lane shoulder width for this entrance ramp is zero (0).

Proposed Condition: The proposed improvement will reduce the outside shoulder along the ramp acceleration lane to 3 feet for approximately 1,200 feet after creation ofthe acceleration lane. The ramp approaching the acceleration lane shoulder width varies, with the narrowest width being 4 feet. Overall, this is not a negative impact on access to emergency incidents and has been agreed upon by the Virginia State Police and District Director of Service Safety. All emergency responders will be informed of the improvement and the existing and proposed constraints.

50f5